## Slide 1: SMART ROOM

## Slide 2: About our project model
RESEARCH
We based our research on reducing global warming while implementing the covid protocols.
ABSTRACT
We believe people need more products specifically dedicated to this niche market
DESIGN
Minimalist and easy to use

## Slide 3: what our project does…..
Our project is a portable motion and climate detector which can calculate the number of people present in the room along with sensing the extra data about the indoor space.

## Slide 4
Components used
Pir motion sensor
Ultrasonic sensor
LDR sensor
DHT11 sensor
2 buzzers
Jumper wires
Breadboard
ESP32

## Slide 5
Often in public spaces and professional environments,
when a room is left unoccupied, the climate control and
lighting systems are left on which leads to a wastage
of electricity

## Slide 6
The chief objective of our project was to build an inexpensive
and reliable IoT system that would warn the last user to switch
off the air conditioning and lights. Which would eventually
help in reducing global warming.

## Slide 7
APPLICATIONS
Due to the versatile and general design of our project, it is possible to deploy it in a multitude of different applications with minimal changes including, but not limited to:-
Dangerous work environments or isolated laboratories
Home security systems
Offices and workspaces
Automatic thermostat system

## Slide 8: OVERVIEW

## Slide 9
FUNCTIONAL OVERVIEW OF OUR PROJECT
People detection by motion sensor
Door open/close detection by ultrasonic
Temperature detection using DHT sensor
Light detection using LDR.
Alarm when utilities are being used in an inefficient manner.
Data collected uploaded to om2m and thing speak.

## Slide 10: Working principle
  The ultrasonic sensor detects when the door is opened or closed
  The pir sensor is used to detect the direction of movement of the person by detecting if there is motion inside the room
  The data from both sensors is combined to increment or decrement the global counter of the number of occupants in the room
  When the count is zero, we check if the lights and air conditioning are turned off, and if not, we sound the buzzer to remind the person leaving last to turn them off
  When the room occupancy is more than the threshold value, then the second buzzer will be turned on

## Slide 11
PROJECT
DEMONSTRATION

## Slide 13: As a secondary goal, we take the data collected by the temperature and light sensors and store it on the cloud to be processed for analytics later.
Data collection

## Slide 17
Our project is capable of collecting large amounts of data about any indoor space it is deployed, thus not only is it useful as an active IoT device, but it is also convenient to deploy as a passive data collection unit.
Potential applications are:-
Mapping out room usage frequency for an entire building
Real-time space management and efficient resource allocation
Mapping the climate of an indoor space to the number of occupants
Pandemic preventative programs
DATA ANALYTICS

## Slide 18: Our project offers a convenient way to limit the number of people present in an enclosed space and monitor the temperature. Needless to say, this is extremely useful for dealing with endemics and pandemics like covid-19 and monkeypox

## Slide 19: Why is our device better?
The products available on the market are either PIR or Ultrasonic or Dual Technology based. Whereas, we use a combi of PIR and Ultrasonic to minimize the errors as much as possible.
The cost of our device would be around $10 which is far more cheaper than the present market products that cost around $100.
The utilization of occupancy sensors helps reduce electricity and running costs to a great extent. Rising demand for energy-efficient sensing solutions to keep the building occupants comfortable and safe is the major factor boosting the occupancy sensor market growth.

## Slide 20: THANK YOU